## Slide 1: How to Create Digital Camera with STM32F4 Discovery Board
Takeshi. I

## Slide 2: Outline
Overview
Device Control and Hardware Connection
Dataflow
Software Architecture
Software Design
Appendix
  Hardware configurations
  Port map

## Slide 3: Overview

## Slide 4: Policy
This is just a hobby project
  Cortex-M (STM32) is not the best choice for digital cameras
  Better to use more powerful SoC such as Cortex-A (e.g. Raspberry Pi)
Little effort on hardware work
  Use discovery board
Do not pursue performance
  Many people already worked on this

## Slide 5: Photos

## Slide 6: Videos
Links to youtube to be here

## Slide 7: Key Components
STM32F4 Discovery Board
  STM32F407VGT (Cortex-M4)
  1-Mbyte Flash memory
  192-Kbyte RAM
Display module
  3.2 inch LCD
  ILI9341 controller
  16-bit parallel I/F
  SD Card socket
Camera module
  OV7670
  Without FIFO

## Slide 8: Specifications
Still photo capture
  JPEG (*.jpg)
  QVGA (320x240)
Movie record
  Motion JPEG (*.avi)
  QVGA (320x240)
  Around 5 fps
Playback
  JPEG (up to 2560x1920)
  RGB565 (320x240)
  Motion JPEG (around 10 fps)
Media
  SD Card (FAT32 format only?, 8GB ~ 16GB of SD card works well)

## Slide 9: Control
SD Card
Capture button
Mode change button
Button
Movie Record @ Liveview mode
Movie Play/Pause @ Playback mode
Dial
JPEG Quality @ Liveview mode
Next content @ Playback mode

## Slide 10: Device Control and Hardware Connection

## Slide 11: Display module (1) – Access sequence
Summary of ILI9341access sequence
  CS (Chip Select) is low during access
  Write access: latch at WRX rising
  Read access: latch at RDX rising
  Command access: DCX is low
  Data access: DCX is high
Write sequence of ILI9341
This is the same access sequence as SRAM
  Regard DCX as address bit, then
  Access LCD module as 1-bit SRAM
Read sequence of ILI9341
*ILI9341 datasheet

## Slide 12: Display module (2) – FSMC function on STM32
STM32 has a function called FSMC (flexible static memory controller), which can be used to control LCD as well
*AN2790 Application note
RS = DCX
STM32F407 memory map
FSMC is assigned from 0x60000000 on STM32
LCD access via FSMC is the same as accessing
  * (volatile uint16_t*)0x6000_0000 for command
  * (volatile uint16_t*)0x6002_0000 for data
The following is the config for this
  Memory Data Width = 16bit
  RS(DCX) is connected to A16
  CS is connected to NE1 (use FSMC bank1)
Note (why 0x60020000???)
  In 16-bit mode, data address issued to the memory is HADDR[25:1] >> 1
  Therefore, in order to set A16 pin to high, CPU needs to access 0x6002_0000 (17-th bit is high)

## Slide 13: Camera module– OV7670 Interface
Control I/F
  SCCB (SIO_C, SIO_D)
Clock supply
  Supply around 24MHz clock (XCLK)
Sync
  OV7670 outputs PCLK, HREF and VSYNC
Pixel data
  OV7670 outputs 8bit data (D[7:0]
*OV7670 datasheet
Use I2C (SCCB is similar to I2C, but NAK)
(Note: need a trick in implementation)
Use MCO (microcontroller clock output) with appropriate pre-scaler
Use DCMI (Digital Camera Interface)

## Slide 14: Other devices
SD Card
  Use SPI
  (wanted to use SDIO, but some pins are shared with DCMI)
Buttons
  Use GPIO
Dial (Rotary Encoder)
  Use TIMER as an external incremental encoder

## Slide 15: Hardware Connection
STM32F4 Discovery
Camera (OV7670)
LCD (ILI9341)
DCMI
I2C
MCO
SCL/SDA
MCLK
pclk, vsync, href
D[0:7]
FSMC
D[0:15]
CS, RS, WR, RD
SD Card
SPI
CS, SCK, MOSI, MISO
Button
Rotary encoder
A/B
TIMER
GPIO
* Be careful of unused on-board devices and function pins
- must avoid using important function pins (e.g. debug pins(SWD))
- some pins might be pulled-up or pulled-down on board
- disable unused devices (e.g. CS for LIS302dl must be always High)

## Slide 16: Port map and used-modules in STM32

## Slide 17: Breakout boards
breakout board for LCD
(connected to the bottom side of Discovery board)
breakout board for Camera
(connected to the front side of Discovery board)
Note1: Wire USART2 on STM32
Note2: Use low profile socket for camera breakout board

## Slide 18: Dataflow

## Slide 19: Main ideas for dataflow
Liveview
  Both ILI9341 and OV7670 support RGB565 format
  So, directly transfer pixel data from OV7670 to ILI9341 using DMA
Still photo capture
  [Problem]
    Not enough space for frame buffer memory (320x240x2)
  [Solution A]
    Increase H blanking time, then encode jpeg line by line
    See the picture on the right
    -> rejected because of too complex control
  [Solution B]
    Use RAM in ILI9341 as frame buffer
    See the picture on the following page
    -> adopt this idea
Movie record
  Repeat still photo capture every frame
  The key point is to start/stop capture from camera frame by frame (do not use continuous capture), so that pixel data in Display is not corrupt during encoding
Line(0)
Line(1)
Line(2)
Line(239)
H blanking
H blanking
H blking
H blking
V blanking
…
1 frame from camera
Encode line(0) during here

## Slide 20: Dataflow - Liveview
STM32F4 Discovery
Camera (OV7670)
LCD (ILI9341)
DCMI
I2C
MCO
SCL/SDA
MCLK
pclk, vsync, href
D[0:7]
FSMC
D[0:15]
CS, RS, WR, RD
SD Card
SPI
CS, SCK, MOSI, MISO
Button
Rotary encoder
A/B
TIMER
GPIO
DMA
RGB565
GRAM

## Slide 21: Dataflow – Still photo capture (JPEG)
STM32F4 Discovery
Camera (OV7670)
LCD (ILI9341)
DCMI
I2C
MCO
SCL/SDA
MCLK
pclk, vsync, href
D[0:7]
FSMC
D[0:15]
CS, RS, WR, RD
SD Card
SPI
CS, SCK, MOSI, MISO
Button
Rotary encoder
A/B
TIMER
GPIO
libjpeg
RGB888
JPEG
GRAM
Use GRAM in LCD as frame buffer
img.jpg
Stop capture from camera during encoding so that GRAM in LCD is kept clean

## Slide 22: Dataflow – Movie recording (Motion JPEG) - 1
STM32F4 Discovery
Camera (OV7670)
LCD (ILI9341)
DCMI
I2C
MCO
SCL/SDA
MCLK
pclk, vsync, href
D[0:7]
FSMC
D[0:15]
CS, RS, WR, RD
SD Card
SPI
CS, SCK, MOSI, MISO
Button
Rotary encoder
A/B
TIMER
GPIO
DMA
(copy only one frame)
GRAM
updated
Repeat 1 and 2
RGB565

## Slide 23: Dataflow – Movie recording (Motion JPEG) - 2
STM32F4 Discovery
Camera (OV7670)
LCD (ILI9341)
DCMI
I2C
MCO
SCL/SDA
MCLK
pclk, vsync, href
D[0:7]
FSMC
D[0:15]
CS, RS, WR, RD
SD Card
SPI
CS, SCK, MOSI, MISO
Button
Rotary encoder
A/B
TIMER
GPIO
libjpeg
RGB888
JPEG
GRAM
img.avi
frame00.jpg
frame01.jpg
frameXX.jpg
…
Img.avi is motion jpeg format, which is a combination of several jpeg files
Repeat 1 and 2
Stop capture from camera during encoding so that GRAM in LCD is kept clean

## Slide 24: Software Architecture

## Slide 25: Software Development Environment
Software Development Environment
  IDE: sw4STM32
  Tools: HAL with STM32 CubeMX
Libraries (Middlewares)
  FreeRTOS
  FatFS
  LibJPEG
Porting and modification needed (not described in this document)
  FatFS porting to use SPI
  LibJPEG modification to use appropriate buffer size
  printf (putc, getc) porting to use UART

## Slide 26: Software Architecture (1) - Policy
Software architecture policy
  Try to abstract device access
    Create my own HAL layer (Display, Camera), which is different from “HAL” from STM32 (call this Stm32HAL)
      STM32HAL abstracts hardware access on SoC such as GPIO
      “My” HAL abstracts external device access such as display (more like BSP)
    Application layer never access driver layer nor Stm32HAL directly
Application layer
HAL (Hardware Abstraction Layer)
Driver layer
Able to reuse the same device driver for another application or project as long as on STM32HAL
No need to modify this layer when I use another device

## Slide 27: Software Architecture (2) - Overview
ModeMgr
LiveviewCtrl
PlaybackCtrl
Display
Camera
OV7670
ILI9341
Application
HAL
Driver
STM32HAL
FreeRTOS
FatFS
Libraries
Modules in red ink has a task
Communication b/w tasks is message
LibJPEG
Service
Input
DebugMonitor
File

## Slide 28: Software Architecture (3) - Responsibility
Application
  ModeMgr: controls mode (Liveview and Playback), runs sequence during mode change
  LiveviewCtrl, PlaybackCtrl: main process in each mode, including enc/dec process
  DebugMonitor: offers test command on terminal (UART). Able to access any module exceptionally
HAL
  Display: abstracts ILI9341 driver
  Camera: abstracts OV7670 driver
Service
  Input: notifies key/dial device status to application (like “C” in MVC)
  File: easy access to filesystem(FatFS)
Driver
  ILI9341: is a device driver for ILI9341
  OV7670: is a device driver for OV7670

## Slide 29: Software Design

## Slide 30: APIs
Module | Queue ID | Command
ModeMgr | QUEUE_MODE_MGR | 
LiveviewCtrl | QUEUE_LIVEVIEW_CTRL | CMD_START CMD_STOP
PlaybackCtrl | QUEUE_CAPTURE_CTRL | CMD_START CMD_STOP
Input | QUEUE_INPUT | CMD_REGISTER CMD_UNREGISTER

## Slide 31: Input
Module X
Input
CMG_REGISTER (key1)
check all input devices
CMD_NOTIFY_INPUT
(key1, status)
1.
ModuleX registers input event
sleep(50msec)
2.
Input periodically checks input device status
loop
3.
if key1 status changed, send status to ModuleX
The input module abstracts input devices
  Button(GPIO) → Key
  Rotary Encoder → Dial
Don’t use interrupt to check input device status
  To avoid disturbing other critical process such as camera control
CMG_UNREGISTER (key1)
4.
ModuleX unregisters input event when no longer needed

## Slide 32: Mode Manager
Liveview mode
Playback mode
boot
Mode key pressed
Mode key pressed
1. Inactivate LiveviewCtrl
2. Activate PlaybackCtrl
1. Inactivate PlaybackCtrl
2. Activate LiveviewCtrl

## Slide 33: LiveviewCtrl : State Machine
INACTIVE
ACTIVE
boot
CMD_START
SINGLE_CAPTURING
MOVIE_RECORDING
CMD_STOP
CMD_NOTIFY_INPUT
(KEY_CAP)
Encode done
CMD_NOTIFY_INPUT
(OTHER0_KEY)
CMD_NOTIFY_INPUT
(OTHER0_KEY)
Not in liveview mode
LIveview
JPEG capture
AVI(Motion JPEG) record every frame

## Slide 34: LiveviewCtrl : Liveview sequence
HW:VSYNC
ModeMgr
LiveviewCtrl
Camera
Display
HW: Camera
HW: Display
Frame(0)
Frame(0)
Frame(1)
Frame(1)
Frame(2)
Frame(2)
CMD_START
Input
KEY_MODE
Initialize()
start_capture()
- continuous
- destination is Display
Transferred by DMA
CMD_STOP
KEY_MODE
stop_capture()
COMP
COMP
HAL_DCMI_Stop() seems a blocking function until next vsync interrupt

## Slide 35: LiveviewCtrl : JPEG Capture sequence
Frame(n)
Frame(n)
KEY_CAP
stop_capture()
f_open()
readOneLine()
Use GRAM in Display as a frame buffer
jpegEncLine()
loop(240 (=height))
f_close()
start_capture()
- continuous
- destination is Display
Stop liveview
Restart Liveview
Frame(n-1)
Frame(n-1)
Frame(n+2)
Frame(n+2)
HW:VSYNC
LiveviewCtrl
Camera
Display
HW: Camera
HW: Display
Input
File
Jpeg file created

## Slide 36: LiveviewCtrl : Movie Record sequence
Frame(n)
Frame(n)
KEY_REC
stop_capture()
f_open()
readOneLine()
jpegEncLine()
start_capture()
- single
readOneLine()
jpegEncLine()
start_capture()
- single
readOneLine()
jpegEncLine()
Frame(n+1)
Frame(n+1)
Frame(n+2)
Frame(n+2)
FrameReady
FrameReady
Display keeps frame image data until each frame encode done as it is Single mode
HW:VSYNC
LiveviewCtrl
Camera
Display
HW: Camera
HW: Display
Input
File
loop(240 (=height))
loop(240 (=height))
loop(240 (=height))

## Slide 37: PlaybackCtrl : StateMachine
INACTIVE
ACTIVE
boot
CMD_START
MOVIE_PLAYING
MOVIE_PAUSE
CMD_STOP
CMD_NOTIFY_INPUT
(OTHER0_KEY)
Not in playback mode
CMD_NOTIFY_INPUT
(OTHER0_KEY)
New content is movie
Reached the end of movie ||
CMD_NOTIFY_INPUT (DIAL)
CMD_NOTIFY_INPUT (DIAL)
If jpeg: display jpeg
If avi : change status
Display next jpeg in motion jpeg file every frame

## Slide 38: Hardware Configurations

## Slide 39: FSMC (for LCD(ILI9341))
FSMC_NORSRAM_TimingTypeDef Timing;
/** Perform the SRAM1 memory initialization sequence
*/
hsram1.Instance = FSMC_NORSRAM_DEVICE;
hsram1.Extended = FSMC_NORSRAM_EXTENDED_DEVICE;
/* hsram1.Init */
hsram1.Init.NSBank = FSMC_NORSRAM_BANK1;
hsram1.Init.DataAddressMux = FSMC_DATA_ADDRESS_MUX_DISABLE;
hsram1.Init.MemoryType = FSMC_MEMORY_TYPE_SRAM;
hsram1.Init.MemoryDataWidth = FSMC_NORSRAM_MEM_BUS_WIDTH_16;
hsram1.Init.BurstAccessMode = FSMC_BURST_ACCESS_MODE_DISABLE;
hsram1.Init.WaitSignalPolarity = FSMC_WAIT_SIGNAL_POLARITY_LOW;
hsram1.Init.WrapMode = FSMC_WRAP_MODE_DISABLE;
hsram1.Init.WaitSignalActive = FSMC_WAIT_TIMING_BEFORE_WS;
hsram1.Init.WriteOperation = FSMC_WRITE_OPERATION_ENABLE;
hsram1.Init.WaitSignal = FSMC_WAIT_SIGNAL_DISABLE;
hsram1.Init.ExtendedMode = FSMC_EXTENDED_MODE_DISABLE;
hsram1.Init.AsynchronousWait = FSMC_ASYNCHRONOUS_WAIT_DISABLE;
hsram1.Init.WriteBurst = FSMC_WRITE_BURST_DISABLE;
hsram1.Init.PageSize = FSMC_PAGE_SIZE_NONE;
/* Timing */
Timing.AddressSetupTime = 2;
Timing.AddressHoldTime = 15;
Timing.DataSetupTime = 4;
Timing.BusTurnAroundDuration = 1;
Timing.CLKDivision = 16;
Timing.DataLatency = 17;
Timing.AccessMode = FSMC_ACCESS_MODE_A;
Need tuning depending on display device spec

## Slide 40: DCMI (for Camera(OV7670))
hdcmi.Instance = DCMI;
hdcmi.Init.SynchroMode = DCMI_SYNCHRO_HARDWARE;
hdcmi.Init.PCKPolarity = DCMI_PCKPOLARITY_RISING;
hdcmi.Init.VSPolarity = DCMI_VSPOLARITY_HIGH;
hdcmi.Init.HSPolarity = DCMI_HSPOLARITY_LOW;
hdcmi.Init.CaptureRate = DCMI_CR_ALL_FRAME;
hdcmi.Init.ExtendedDataMode = DCMI_EXTEND_DATA_8B;
hdcmi.Init.JPEGMode = DCMI_JPEG_DISABLE;
hdma_dcmi.Instance = DMA2_Stream1;
hdma_dcmi.Init.Channel = DMA_CHANNEL_1;
hdma_dcmi.Init.Direction = DMA_PERIPH_TO_MEMORY;
hdma_dcmi.Init.PeriphInc = DMA_PINC_DISABLE;
hdma_dcmi.Init.MemInc = DMA_MINC_DISABLE;
hdma_dcmi.Init.PeriphDataAlignment = DMA_PDATAALIGN_WORD;
hdma_dcmi.Init.MemDataAlignment = DMA_MDATAALIGN_WORD;
hdma_dcmi.Init.Mode = DMA_NORMAL;
hdma_dcmi.Init.Priority = DMA_PRIORITY_LOW;
hdma_dcmi.Init.FIFOMode = DMA_FIFOMODE_DISABLE;

## Slide 41: Port map

## Slide 42: Port map
## IO
PA00 = ROTARY_A (TIM5_CH1) ! pulled-up on board
PA01 = ROTARY_B (TIM5_CH2)
PA02 = USART2 (TX)
PA03 = USART2 (RX)
PA04 = CAMERA_HS(DCMI_HSYNC)
PA05 = SD_CARD(SPI1_SCK)
PA06 = CAMERA_PCLK(DCMI_PIXCK)
PA07 = SD_CARD(SPI1_MOSI)
PA08 = CAMERA_MCLK(MCO1)
PA09 = [VBUS_FS]
PA10 = [OTG_FS_ID]
PA11 = [OTG_FS_DM]
PA12 = [OTG_FS_DP]
PA13 = [SWDIO]
PA14 = [SWCLKDebug]
PA15 = SD_CARD(SPI1_NSS(SW control))
PB00 = N/A
PB01 = N/A
PB02 = [BOOT]
PB03 = [SWO]
PB04 = SD_CARD(SPI1_MISO)
PB05 = N/A
PB06 = CAMERA_D5(DCMI_D5)
PB07 = CAMERA_VS(DCMI_VSYNC)
PB08 = CAMERA_D6(DCMI_D6)
PB09 = CAMERA_D7(DCMI_D7)
PB10 = CAMERA(I2C2_SCL)
PB11 = CAMERA(I2C2_SDA)
PB12 = N/A
PB13 = N/A
PB14 = N/A
PB15 = N/A
PC00 = [OTG_FS_PowerSW] !Don't use
PC01 = BUTTON1
PC02 = BUTTON2
PC03 = BUTTON3
PC04 = N/A
PC05 = CAMERA_RESET
PC06 = CAMERA_D0(DCMI_D0)
PC07 = CAMERA_D1(DCMI_D1)
PC08 = CAMERA_D2(DCMI_D2)
PC09 = CAMERA_D3(DCMI_D3)
PC10 = [CS43L22_SCLK] !Don't use
PC11 = CAMERA_D4(DCMI_D4)
PC12 = [CS43L22_SDIN] !Don't use
PC13 = N/A
PC14 = [OSC32_IN]
PC15 = [OSC32_IN]
PD00 = LCD_D2(FSMC_D2)
PD01 = LCD_D3(FSMC_D3)
PD02 = N/A
PD03 = N/A
PD04 = LCD_RD(FSMC_NOE)
PD05 = LCD_WD(FSMC_NWE)
PD06 = N/A
PD07 = LCD_CS(FSMC_NE1)
PD08 = LCD_D13(FSMC_D13)
PD09 = LCD_D14(FSMC_D14)
PD10 = LCD_D15(FSMC_D15)
PD11 = LCD_RS(FSMC_A16)
PD12 = LED
PD13 = LED
PD14 = LED, LCD_D0(FSMC_D0)
PD15 = LED, LCD_D1,(FSMC_D1)
PE00 = [LIS302DL_INT1] !Don't use
PE01 = [LIS302DL_INT2] !Don't use
PE02 = [LIS302DL_CS] !Always HIGH
PE03 = N/A
PE04 = N/A
PE05 = N/A
PE06 = N/A
PE07 = LCD_D4(FSMC_D4)
PE08 = LCD_D5(FSMC_D5)
PE09 = LCD_D6(FSMC_D6)
PE10 = LCD_D7(FSMC_D7)
PE11 = LCD_D8(FSMC_D8)
PE12 = LCD_D9(FSMC_D9)
PE13 = LCD_D10(FSMC_D10)
PE14 = LCD_D11(FSMC_D11)
PE15 = LCD_D12(FSMC_D12)
## Function
USART2 = TERMINAL
SPI1 = SD CARD
I2C2 = CAMERA(OV7670)
FSMC = LCD(ILI9341)
DCMI = CAMERA(OV7670)
TIMER5_CH1/2 = Rotary Encoder
## DMA
DMA1_5 = USART2_RX
DMA2_1 = CAMERA(DCMI->FSMC(LCD))
## OSC
PH0 = OSC_IN (external 8MHz)
PH1 = OSC_OUT (external 8MHz)
## Note
LCD_RESET = VDD
CAMERA_PWDN = GND

## Slide 43: backup

## Slide 44: APIs
Module | Queue ID | COMMAND
modeMgr | QUEUE_MODE_MGR | NOTIFY_EXIT
liveviewCtrl | QUEUE_LIVEVIEW_CTRL | START STOP
captureCtrl | QUEUE_CAPTURE_CTRL | START
playbackCtrl | QUEUE_CAPTURE_CTRL | START STOP
input | QUEUE_INPUT | REGIST UNREGIST
modeMgr sends these messages when mode changed
When a control module exits (by itself?), the control module sends this message
Any module which wants to be notified input status calls this

## Slide 45: Software structure (to be)
Application layer
HAL (Hardware Abstraction Layer)
Driver layer
OV7670
ILI9341

## Slide 46: Software structure
modeMgr
liveviewCtrl
+ init()
+ enter()
+ exit()
captureCtrl
+ init()
+ enter()
+ exit()
playbackCtrl
+ init()
+ enter()
+ exit()
display
camera
input
ov7670
ili9341
app
hal
driver
STM32 lib
FatFS
libJPEG
library
debugMonitor

## Slide 47: Software structure
modeMgr
liveviewCtrl
captureCtrl
playbackCtrl
display
camera
input
ov7670
ili9341
app
hal
driver
STM32 lib
FatFS
libJPEG
Middleware
Modules in red ink has each task
Communication is done by message queue instead of function call
debugMonitor

## Slide 48: Software structure (current test program)
main()
OV7670
ILI9341

## Slide 49: Overview (HW)
test

## Slide 50: Overview (HW)
test

## Slide 51: Overview (HW)
test